## Slide 1
&morphometry
latitude
longitude
In the morphometry section, there are parameters for latitude and longitude, but I don’t know whether they are used
glm3.nml

## Slide 2
base_elev
(sea level)
crest_elev
The base elevation of the lake is the height above sea level.
(You will have to correspond to the lowest height that you set with the first input in H).
&morphometry
glm3.nml

## Slide 3
&morphometry
bsn_len
There are parameters to do with basin length and width,
which have something to do with inflow and outflow,
but no one really knows what they are for.
bsn_wid
glm3.nml

## Slide 4
H =
50.1
30.2,
20.8,
10.5,
10.0,
0.0,
A =
5000
1000,
500,
200,
100,
0.0,
You set the heights and areas using H (m) and A (m2).
The sequence of H corresponds to the sequence of A.
&morphometry
glm3.nml

## Slide 5
You can set the file names and numbers of river inflows.
The inflow files can contain flow of water, along with other variables, such as temperature and salinity.
&inflow
inflow_fl = ‘bcs/file1.scv’,
‘bcs/file2.scv’,
‘bcs/file3.scv’,
‘bcs/file4.scv’,
‘bcs/file5.scv’
num_inflows = 3
glm3.nml

## Slide 6
Just like the inflows, you can set the outflows, with file names, numbers of outflows, and variables in each file. Outflow has a height. No one knows whether there is an equivalent inflow height.
&outflow
outflow_fl = ‘bcs/file1.scv’,
‘bcs/file2.scv’,
‘bcs/file3.scv’,
‘bcs/file4.scv’,
‘bcs/file5.scv’
num_inflows = 2
glm3.nml

## Slide 7
10 m
20 m
30 m
10 °C
18 °C
25 °C
You can set the initial conditions for temperature and salinity at some points that you choose, and the model will interpolate between them.
&init_profiles
lake_depth
the_depths =
30.0
20.0,
10.0,
1.0,
the_temps =
25
18,
10,
0.0,
the_sals =
1
10,
34,
35,
Temperature at this depth at time 0
1 m
glm3.nml

## Slide 8
10 m
20 m
30 m
10 °C
18 °C
25 °C
Temperature at this depth at time 0
If you have a list of initial condition points, you can select the number of depths in that list that you want to use, starting at the beginning of the list.
lake_depth
the_depths =
30.0
20.0,
10.0,
1.0,
the_temps =
25
18,
10,
0.0,
num_depths = 4
4
3
2
1
1 m
&init_profiles
glm3.nml

## Slide 9
10 m
20 m
30 m
10 °C
18 °C
25 °C
Temperature at this depth at time = 0
This height doesn’t exist, so it breaks the model
If you lower the initial lake height between simulations,
you have to check the initial profiles.
the_depths =
30.0
20.0,
10.0,
0.0,
&init_profiles
glm3.nml

## Slide 10
10 m
20 m
30 m
10 °C
18 °C
25 °C
Temperature at this depth at time = 0
This height doesn’t exist, so it breaks the model
If you lower the initial lake height, you could reduce the number of initial profile depths.
the_depths =
30,
20.0,
10.0,
0.0
num_depths = 3
4
3
2
1
&init_profiles
glm3.nml

## Slide 11
The model also has sediment zones.
You set the upper depth levels of the zones.
Zone 4
Zone 5
&sediment
Zone 3
Zone 2
Zone 2
Zone 3
Zone 4
Zone 5
Zone 1
zone_heights =
50
40,
30,
20,
10,
The depths of the zones are actually:
40 to 50 m
30 to 40 m,
20 to 30 m,
10 to 20 m,
0 to 10 m,
glm3.nml

## Slide 12
In a list of sediment zone upper heights,
you can set the number of zones that you want to use.
Zone 4
Zone 5
Zone 3
Zone 2
Zone 2
Zone 3
Zone 4
Zone 5
Zone 1
zone_heights =
50
40,
30,
20,
10,
num_zones = 5
5
4
3
2
1
&sediment
glm3.nml

## Slide 13
If you were to view a lake from the air,
and if you could see contours,
the sediment zones might look like this
Zone 1
Zone 2
Zone 3
Zone 4
Zone 5
&sediment
glm3.nml

## Slide 14
Zone 4
Zone 3
Zone 2
Zone 2
Zone 3
Zone 4
Zone 1
Zone 4
Zone 3
Zone 2
Zone 2
Zone 3
Zone 4
Zone 1
The lake depth layers are completely horizontal
and several depth layers correspond to separate sediment zones
It is not set up as though the bottommost lake layer corresponds to all of the sediment

## Slide 15
This height doesn’t exist, so it breaks the model
You have to set the number of sediment zones to match your initial profile.
If you change the initial height, be careful about dropping the initial lake height.
30 m
25 °C
&init_profiles
Zone 4
Zone 5
Zone 3
Zone 2
Zone 2
Zone 3
Zone 4
Zone 5
Zone 1
lake_depth
zone_heights =
50
40,
30,
20,
10,
num_zones = 4
therefore, reduce the number of zones, or drop the zone height to correspond to lake_depth
5
4
3
2
1
&sediment
glm3.nml

## Slide 17
10 m
18 m
&output
csv_point_at =
29
18,
10,
5,
csv_lake_fname
5 m
29 m
out_fn
There are three types of output: 1) out_fn is a netcdf of all depths and times
2) csv_lake_name is for the surface properties and
3) csv_point_at is at specified depths and variables
glm3.nml

## Slide 18
10 m
18 m
csv_point_at =
29
18,
10,
5,
csv_point_nlevs = 4
4
3
2
1
5 m
29 m
csv_point_nvars = 2
csv_point_vars = ‘temp’, ‘salt’, ‘oxy’
csv_point_vars = ‘temp’, ‘salt’, ‘oxy’
csv_point_vars = ‘temp’, ‘salt’, ‘oxy’
csv_point_vars = ‘temp’, ‘salt’, ‘oxy’
The number of csv_point_at points in the list is set with csv_point_nlevs and
the number of variables in the list is set with csv_point_nvars.
&output
glm3.nml

## Slide 19
This height doesn’t exist, so it breaks the model
If you lower the initial lake height, you have to check csv output levels.
&init_profiles
lake_depth
10 m
18 m
5 m
29 m
csv_point_at =
29
18,
10,
5,
csv_point_nlevs = 3
therefore, reduce the number of levels
4
3
2
1
&output
glm3.nml

## Slide 20
There is a large structure called ‘candi’, which contains all of the reactions, rates, parameters etc.
The matrix of chemical variable concentrations is called ‘y’.
The parameters are all in the section ‘param’. If you want to access the parameters, you use ‘candi%param’.
If you want to select the kinetic rate constant for ammonium oxidation, you use candi%param%knh4ox
candi =
param + reac + y + ydot + …
reac
param
y

## Slide 21
In aed2_sedcandi, there is a variable called ‘y’.
It contains all of the sediment chemical variables at all depths.
It gets updated at every time step.
y at any one time step =
If you just want ammonium concentration, then you ask for candi%y(candi%nh4y , : ). In this case, the index happens to be 5.
The rows are assigned during initialization, according to the order given in aed2.nml / variables
The concentrations assigned to each variable are given by aed2.nml / initial_vals
 |  | Variables |  |  |  |  |  |  |  | 
 |  | Solutes | dcolmap = dissConcs |  | Solids | pcolmap = partConcs |  |  |  | 
 |  | … | oxy | amm | poml | feoh3a | … | pH | pe | ubalchg
 |  | startSedCol | 2 | 5 | 25 | 37 | endSedCol | nvars+1 | nvars+2 | nvars+3
Depths | bottomConcs depths |  | default_vals(2) | default_vals(5) | default_vals(25) | default_vals(37) |  | 7.9 | 8.0 | 0.0
 | kk | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+1 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+2 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+3 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+4 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+5 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+6 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+7 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | … |  |  |  |  |  |  |  |  | 
 | maxnpts | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0

## Slide 22
The initial concentration for each species is set using initial_vals.
It is a constant concentration with depth.
concentration
depth
One day, we will set up the initial condition to read a concentration profile from a file.

## Slide 23
 |  | Variables |  |  |  |  |  |  |  | 
 |  | Solutes | dcolmap = dissConcs |  | Solids | pcolmap = partConcs |  |  |  | 
 |  | … | oxy | amm | poml | feoh3a | … | pH | pe | ubalchg
 |  | startSedCol | 2 | 5 | 25 | 37 | endSedCol | nvars+1 | nvars+2 | nvars+3
Depths | bottomConcs depths |  | default_vals(2) | default_vals(5) | default_vals(25) | default_vals(37) |  | 7.9 | 8.0 | 0.0
 | kk | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | 7.9 | 8.0 | 0.0
 | kk+1 | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | 7.9 | 8.0 | 0.0
 | kk+2 | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | 7.9 | 8.0 | 0.0
 | kk+3 | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | 7.9 | 8.0 | 0.0
 | kk+4 | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | 7.9 | 8.0 | 0.0
 | kk+5 | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | 7.9 | 8.0 | 0.0
 | kk+6 | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | 7.9 | 8.0 | 0.0
 | kk+7 | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | 7.9 | 8.0 | 0.0
 | … |  |  |  |  |  |  |  |  | 
 | maxnpts | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | sedimentConcs + reactions | 7.9 | 8.0 | 0.0
ydot at the end of any one time step =
The model calculates all of the
kinetic chemical reactions, then
the equilibrium reactions, then
the physical transport processes.
There is another matrix called ‘ydot’, which accounts for all the changes at the end of the time step.
The model then calculates the new y as
yt = yt-1 + ydot

## Slide 24
Over the course of the simulation, the profiles will emerge to whatever they are going to. They may either accumulate with depth or at the surface.
If the parameter
candi%param%ibbc ≠ 2,
then they could look like this.
concentration
depth
concentration
depth
accumulates with depth
accumulates at the surface

## Slide 25
However, if ibbc = 2, it sets the change between two timesteps at maximum depth to be zero.
That means it holds that bottom concentration to be the same as initial_vals.
For a variable that accumulates with depth, this can lead to a funky result.
concentration
depth
concentration
depth

## Slide 26
Sediment-water connections
Zone 4
Zone 5
Zone 3
Zone 2
Zone 2
Zone 3
Zone 4
Zone 5
Zone 1
default_vals
deep_vals
&aed2_sed_candi
aed2.nml
The simplest way to run the sediment model is by disregarding the lake.
The sediment-water interface is set with default_vals for all solutes (mmol m-3) and solids (mmol m-2 y-1).
The interface beneath the bottommost sediment layer is set using deep_vals, if a positive number is present.
in this case ibc2 = 1 or 2
in this case ibbc = 1

## Slide 27
Zone 4
Zone 3
Zone 2
Zone 2
Zone 3
Zone 4
Zone 1
default_vals

## Slide 28
Zone 4
Zone 3
Zone 2
Zone 2
Zone 3
Zone 4
Zone 1
deep_vals

## Slide 29
 |  | Variables |  |  |  |  |  |  |  | 
 |  | Solutes | dcolmap = dissConcs |  | Solids | pcolmap = partConcs |  |  |  | 
 |  | … | oxy | amm | poml | feoh3a | … | pH | pe | ubalchg
 |  | startSedCol | 2 | 5 | 25 | 37 | endSedCol | nvars+1 | nvars+2 | nvars+3
Depths | bottomConcs depths |  | default_vals(2) | default_vals(5) | default_vals(25) | default_vals(37) |  | 7.9 | 8.0 | 0.0
 | kk | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+1 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+2 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+3 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+4 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+5 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+6 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+7 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | … |  |  |  |  |  |  |  |  | 
 | maxnpts | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
The method of choosing the concentration in the top depth, fixed at each time step, is set using candi%param%ibc2. It could be
0 - linked variables if present; otherwise default_vals
1 – only default_vals
2 – only default_vals, except pomspecial
10 – values from swibc.dat if present; otherwise default-vals
y at the surface layer at every time step
In aed2_seddiagenesis, these are refreshed at every timestep using candi%PartFluxes for solids

## Slide 30
In aed2.nml the variables are listed in sequence
and the corresponding default_vals are listed in the same sequence.
In this example, the third variable, so4, has a top boundary concentration of 229 mmol m-3.

## Slide 31
 |  | Variables |  |  |  |  |  |  |  | 
 |  | Solutes | dcolmap = dissConcs |  | Solids | pcolmap = partConcs |  |  |  | 
 |  | … | oxy | amm | poml | feoh3a | … | pH | pe | ubalchg
 |  | startSedCol | 2 | 5 | 25 | 37 | endSedCol | nvars+1 | nvars+2 | nvars+3
Depths | bottomConcs depths |  | default_vals(2) | default_vals(5) | default_vals(25) | default_vals(37) |  | 7.9 | 8.0 | 0.0
 | kk | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+1 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+2 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+3 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+4 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+5 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+6 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | kk+7 | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
 | … |  |  |  |  |  |  |  |  | 
 | maxnpts | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | sedimentConcs | 7.9 | 8.0 | 0.0
The concentration at the deepest layer could also be set by candi%param%ibbc =
1 – deep_vals if present (>0); otherwise do nothing
2 – fix all of the bottom concs to initial_vals
10 – take it from deepbc.dat if present; otherwise do nothing
This should only apply to dissolved species
y at the deepest layer at every time step

## Slide 32
In aed2.nml the variables are listed in sequence
and the corresponding ‘deep_vals’ are listed in the same sequence.
In this example, the fourth variable, frp, has a bottom boundary concentration of 200 mmol m-3.
The negative values are not used at all, but they need to be there to keep that sequence tied to the ‘variables’ sequence.

## Slide 33
Sediment-water connections
Zone 4
Zone 5
Zone 3
Zone 2
Zone 2
Zone 3
Zone 4
Zone 5
Zone 1
from_bc_file
use_deep_bc
aed2_sediment_swibc.dat
aed2_sediment_deepbc.dat
&aed2_sed_candi
aed2.nml
in this case ibc2 = 10
in this case ibbc = 10
To use a boundary file, you can choose which variables will be taken from that file.
For the upper boundary you can specify those variables using ‘from_bc_file’.
For the lower boundary, it is in ‘use_deep_bc’.

## Slide 34
Zone 4
Zone 5
Zone 3
Zone 2
Zone 2
Zone 3
Zone 4
Zone 5
Zone 1
from_bc_file
use_deep_bc
aed2_sediment_swibc.dat
aed2_sediment_deepbc.dat

## Slide 35
Zone 4
Zone 3
Zone 2
Zone 2
Zone 3
Zone 4
Zone 1
from_bc_file
aed2_sediment_swibc.dat

## Slide 36
Zone 4
Zone 3
Zone 2
Zone 2
Zone 3
Zone 4
Zone 1
use_deep_bc
aed2_sediment_deepbc.dat

## Slide 37
In aed2.nml the boundary condition file variables are not tied to the sequence in ‘variables’.
In this example, only ‘oxy’ is taken from the upper boundary file, while ‘feii’ and ‘h2s’ could be easily turned on.

## Slide 38
In this example, ‘oxy’ boundaries will be used for zones 1, 2, and 3.
The ‘feii’ boundary will be disregarded, because it was not listed in ‘from_bc_file’.
The ‘oxy’ concentration will change at 7 days, 14 days, 21 etc.
These changing times do not have to be regular steps, however, they are the same for all zones.

## Slide 39
For ‘use_deep_bc’ the functionality is the same as ‘from_bc_file’.
In this example, all three of ‘h2s’, ‘frp’ and ‘feii’ will be taken from the deepbc file.

## Slide 40
In this example, all of zones 1, 2, and 3 are used:
‘frp’ in zone 1
‘h2s’ in zone 2 and
‘feii’ in zone 3.
For those variables not specified by zone, they will default to the ‘deep_vals’ values.

## Slide 41
Sediment-water connections
Zone 4
Zone 5
Zone 3
Zone 2
Zone 2
Zone 3
Zone 4
Zone 5
Zone 1
water_link
Zone 4
average
Zone 3
average
Zone 2
average
Zone 1
average
&aed2_sedflux
&aed2_sed_candi
aed2.nml
Another option for the sediment-water interface is to use the lake inputs at the interface.
The lake layers that correspond to each sediment zone will have their concentrations averaged and used as the bottom water concentration.
To switch this on, ibc2 = 0.

## Slide 42
In aed2.nml the variables are listed in sequence
and the corresponding ‘water_link’s are listed in the same sequence.
Any blanks are disregarded and the ‘default_vals’ are used instead.
In this example, only oxygen is linked from the water column, using the linking variable named ‘OXY_oxy’.
The nomenclature indicates the aed2 module aed2oxygen (‘OXY_’)
and the output variable from that module (‘oxy’).

## Slide 43
Sediment-water connections
Zone 4
Zone 5
Zone 3
Zone 2
Zone 2
Zone 3
Zone 4
Zone 5
Zone 1
Zone 4
average of OXY_oxy
Zone 3
average of OXY_oxy
Zone 2
average of OXY_oxy
Zone 1
average of OXY_oxy
&aed2_sedflux
&aed2_sed_candi
aed2.nml
&aed2_oxygen
aed2_oxygen
various oxygen inputs
various other oxygen outputs
The oxygen module will do all of its own calculations in the water column,
and among other things, it will supply average oxygen concentrations to each sediment zone.
We also have to set the parameter ‘sedflux_model’ equal to ‘dyanmic2d’ in the section &aed2_sedflux …

## Slide 44
Dynamic
Dynamic2D
Zone 1
Zone 2
Zone 3
Zone 4
Zone 2
Zone 3
Zone 4
One general sediment zone
Zone 4
Zone 3
Zone 2
Zone 2
Zone 3
Zone 4
Zone 1
Constant2D
Constant
One general sediment zone
When using GLM, there are four options for the parameter ‘sedflux_model’.
The two constant options have one sediment flux value set for the duration of the whole simulation: hence it is constant in time.
The two dynamic options employ the sediment diagenesis model: it is dynamic in the sense that the sediment model will produce changing values over time.

## Slide 45
Sediment-water connections
Zone 4
Zone 5
Zone 3
Zone 2
Zone 2
Zone 3
Zone 4
Zone 5
Zone 1
part_sed_link
Zone 4
average
Zone 3
average
Zone 2
average
Zone 1
average
&aed2_sedflux
&aed2_sed_candi
aed2.nml
To send the water column fluxes of solids to the sediment, use ‘part_sed_link’.

## Slide 46
Sediment-water connections
Zone 4
Zone 5
Zone 3
Zone 2
Zone 2
Zone 3
Zone 4
Zone 5
Zone 1
diss_flux_link
&aed2_sedflux
&aed2_sed_candi
aed2.nml
To send the sediment fluxes of solutes to the water column, use ‘diss_flux_link’.
&aed2_sed_const2d

## Slide 47
You need these namelists and parameters.
The ‘diss_flux_link’ sequence is tied to ‘variables’.
In this example, the second position is matched to ‘oxy’.
The name of the linked variable needs to be the same as set out in the aed2_oxygen namelist.
The number of zones, for our purposes should be defined as the same in both the &aed2_sed_candi namelist and the &aed2_sed_const2d namelist.

## Slide 48
Note that the sediment zones have been specified in three different places:
in glm.nml &sediment n_zones
which sets the zone heights in the lake
in aed2.nml &aed2_sed_candi nZones
which establishes the number of times the diagenesis model runs, and
in aed2.nml &aed2_sed_const2d
which defines which lake variables are linked to which sediment variables
Zone 2
Zone 3
Zone 1

## Slide 49
&output
There are two other types of output: 4) .sed files, separate for each variable, including all depths and times
5) swi_fluxes for the interactions between the bottommost cell of the lake and the uppermost layer of the sediment
Each of these is organized into separate sediment zones.
glm3.nml
Zone 1
Zone 2
glm outputs

## Slide 50
&output
The .sed files contain information for each variable, including all depths and times. They come in three forms:
the concentrations (mmol L-1) of everything specified in ‘default_vals’
reaction rates (mmol L-1 y-1) if they are specified in ‘morevariables’, for example, ‘ROMSO4’
rate limitation factors (unitless, scaling between 0 and 1), if they are specified in ‘morevariables’, for example FIN_NO3. The limitation factors refer to the products of factors such as the Monod limitation, and inhibition by higher energy reactions
glm3.nml
glm outputs

## Slide 51
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | … | output.nc/dim/time/len
The time steps in hours - output.nc/dim/time/vals
1
2
3
4
5
6
7
8
9
10
…
You imagine this: an absolute grid of height in m
The height data, changing over time - output.nc/dim/z/vals
Here is how it deals with depth

## Slide 52
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | … | output.nc/dim/time/len
The time steps in hours - output.nc/dim/time/vals
1
2
3
4
5
6
7
8
9
10
…
An imaginary index of z layers
output.nc/var/OXY_oxy/size/3
Here is how it deals with any one variable, say oxygen
output.nc/var/OXY_oxy/size/4
The oxygen data - output.nc/var/OXY_oxy/vals

## Slide 53
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | … | output.nc/dim/time/len
The time steps in hours - output.nc/dim/time/vals
1
2
3
4
5
6
7
8
9
10
…
An imaginary index of z layers
output.nc/var/OXY_oxy/size/3
So what if you wanted to plot oxygen at the 10th hour for all depths?
output.nc/var/OXY_oxy/size/4
The oxygen data - output.nc/var/OXY_oxy/vals

## Slide 54
This bottom area is effectively lost from the modelling domain
Upon sedimentation, the frame of reference shifts upwards
time = 1
time = 2
time = 3
time = 4

## Slide 55
time = 1
time = 2
time = 3
time = 4
w00
The rate of sedimentation is given by w00, in units of cm y-1.
For a given set of particles at a depth,
as the frame of reference moves up,
those particles move down.
Similarly, any porewater moves, through advection, at the same rate.

## Slide 56
w00
w00
If poreflux is non-zero, then porewater moves at a different rate to w00.
If the poreflux parameter value is positive,
then the porewater moves up relative to the particles.
If the poreflux parameter value is negative,
then the porewater moves down relative to the particles.
poreflux
poreflux

## Slide 58
Sequestered carbon
Organic carbon
Atmospheric carbon
Greenhouse gases